l×@l×@ screen.

First, install theese three good packages:
-less (a pager I like for watching man pages more confortable)
-bzip2 (for uncompressing linrad *tar.bz)
-links ( a good text mode WEB browser for browsing the net)

#apt-get install less bzip2 links

Then install the gcc compiler and all related stuff for compiling:

#apt-get install build-essential

This should take some time (27.8MB) After that, all the great compiling
software from the GNU is ready.

Now, lets download svgalib and linrad. If you do not know where to
download them, use the "links" text mode WEB browser and google for it!

To retrieve the files, use the great "wget" text mode downloading
program. It allows resuming broken downloads. Download the Svgalib and 
Linrad files on your home directory: (note that if your card is 
supported by the old svgalib 1.4.3 that is shipped with Debian, you do 
not need to compile the 1.9.20, but apt-get install the packaged version)

go to your home directory:

$ cd

download the files:

$ wget -c http://www.nitehawk.com/sm5bsz/linuxdsp/archive/lir01-33.tbz

and
$ wget -c http://www.arava.co.il/matan/svgalib/svgalib-1.9.20.tar.gz

If you are using this guide and new Linrad and svgalib are released, you 
can use the "links" text mode WEB browser to surf the Internet and 
search for the new file locations.

For example

$ links http://www.google.com

will start the links text mode browser.


Install nasm package from the debian servers:

# apt-get install nasm



Now, there is a little issue that I found. For compiling svgalib_helper
module, we need the kernel headers. So we will install the package
kernel-headers-2.6.8-2-386. I do not understand why there is NOT a
kernel-headers-2.6.8-1-386 file, to mach the kernel-image-2.6.8-1-386
that was installed by Debian. So, I also installed the matching kernel 
image.

install the headers:

# apt-get install kernel-headers-2.6.8-2-386

and the kernel image that matches with the headers:

#apt-get install kernel-image-2.6.8-2-386

when it asks you "do you want to stop now?--->  SAY "N" and continue.

NOTE: As I do not use any boot loader for my experimental debian setup 
(I boot
if from my other Debian machine) , I can not confirm it, but the new
kernel-image install should modify your grub setting to point to the new
kernel version. If it is not the case, modify /boot/grub/menu.1st to 
point to the new kernel image and initrd image version.
(I would like that someone could verify this)

Now reboot to use the new kernel:

# reboot

When booted, verify that the command:

$ uname -a

gives the 2.6.8-2 version.

Now it is time to install ALSA stuff:

#apt-get install alsa-utils alsa-oss

Note that alsa-utils will install alsa-base as a dependency. Alsa-base 
will prevent from loading the OSS and ALSA drivers at the same
time. (debian uses the "hotplug" and "discover" to do it at boot time).
When installing alsa-base it modifies the "discover" behaviour to
exclude the OSS sound drivers. /etc/discover.d/)

Reboot again just to see everything works.


(This could be really not needed, but it is better to do it to check 
that OSS drivers are unloaded. In my case, before installing ALSA, there 
were OSS and ALSA drivers for my sound card loaded at the same time.

# reboot

Configure the sound card with the "alsaconf" utility. It is very
intuitive to choose your sound card. It will detect it automagically.:

# alsaconf

We are ready to compile svgalib:

Go to the directory in with you have downloaded the sources.


# tar xfvz svgalib-1.9.20
# cd svgalib-1.9.20
# make install
# make demoprogs
# cd demos
# depmod -a

load the svgalib_helper module manually:

# modprobe svgalib_helper

run the test program to see if svgalib works:

# ./vgatest

if it does not work, you should edit /etc/vga/libvga.config file to match
your hardware, but It should do it automatically.


lets test your mouse setup:

#./mousetest

and move your mouse and click  the buttons to see if it works
If it does not work, you have to edit the config file 
/etc/vga/libvga.config and choose your mouse type and mouse device. In 
my case, I commented "mouse Microsoft" and  uncommented "mouse PS2". I 
also changed "/dev/ttyS0" for "/dev/psaux" to point my right mouse PS2 
device.

Now it is ttime to compile Linrad:
Go to your home directory:

$ cd

uncompress the source:

# tar xfvj lir01-33.tbz
# cd linrad-01.33
# ./configure
# make

Note that svgalib_helper module was loaded before.
if not, you can use

#modprobe svgalib_helper

to load it

Run linrad

# ./linrad

and follow Leif directions.

#rmmod svgalib_helper

will unload that module from memory.

You can write a simple bash script and locate it on your linrad 
directory. Call it for example, "runlinrad" and "chmod 755 runlinrad" to 
make it executable.

************************
#!/bin/bash
# script to load module, run linrad, and unload module.
modprobe svgalib_helper
./linrad
rmmod svgalib_helper
************************

So you only need to invoque that script to run Linrad:

./runlinrad

That is all.

Please send me any comments, corrections or suggestions. I will also 
appreciate that you correct my english ;-)

Leif, if possible, I would like to see this guide published somewhere in 
your web page to help Debian hams to setup Linrad.

Thank you very much.

73, Ramiro. EA1ABZ.







#############################################################
This message is sent to you because you are subscribed to
  the mailing list <linrad@antennspecialisten.se>.
To unsubscribe, E-mail to: <linrad-off@antennspecialisten.se>
To switch to the DIGEST mode, E-mail to <linrad-digest@antennspecialisten.se>
To switch to the INDEX mode, E-mail to <linrad-index@antennspecialisten.se>
Send administrative queries to  <linrad-request@antennspecialisten.se>�7ÈHello friends.

I have just installed Linrad perfectly in my new debian experimental 
setup. I have written this little guide, in which it is show how to 
setup svgalib and Linrad in a basic debian text machine.

I asume that you have just installed Debian Sarge with the rc-3
installer. I also asume  (it was my case) that the Debian installation
was made without internet access and that you have a modem. If you
installed Debian trough the Internet by other methods, you should have
an Internet connection running. Lets go!


Configure the internet access:

#apt-get install pppconfig
#pppconfig

and answer the questions to create a new Internet connection. If you
want to be able to start the internet session as a normal user (not only
as root), do not forget to select in the advanced options: "add user"

to start the modem connection, send the command (you do not need to be 
root):

$ pon

Well, we are on the Internet.

Now, configure the mirrors from wich apt will download the files:

# apt-setup

choose the desired ftp mirrors on the dialog screen.

First, install theese three good packages:
-less (a pager I like for watching man pages more confortable)
-bzip2 (for uncompressing linrad *tar.bz)
-links ( a good text mode WEB browser for browsing the net)

#apt-get install less bzip2 links

Then install the gcc compiler and all related stuff for compiling:

#apt-get install build-essential

This should take some time (27.8MB) After that, all the great compiling
software from the GNU is ready.

Now, lets download svgalib and linrad. If you do not know where to
download them, use the "links" text mode WEB browser and google for it!

To retrieve the files, use the great "wget" text mode downloading
program. It allows resuming broken downloads. Download the Svgalib and 
Linrad files on your home directory: (note that if your card is 
supported by the old svgalib 1.4.3 that is shipped with Debian, you do 
not need to compile the 1.9.20, but apt-get install the packaged version)

go to your home directory:

$ cd

download the files:

$ wget -c http://www.nitehawk.com/sm5bsz/linuxdsp/archive/lir01-33.tbz

and
$ wget -c http://ww	\\×@\×@l/matan/svgalib/svgalib-1.9.20.tar.gz

If you are using this guide and new Linrad and svgalib are released, you 
can use the "links" text mode WEB browser to surf the Internet and 
search for the new file locations.

For example

$ links http://www.google.com

will start the links text mode browser.


Install nasm package from the debian servers:

# apt-get install nasm



Now, there is a little issue that I found. For compiling svgalib_helper
module, we need the kernel headers. So we will install the package
kernel-headers-2.6.8-2-386. I do not understand why there is NOT a
kernel-headers-2.6.8-1-386 file, to mach the kernel-image-2.6.8-1-386
that was installed by Debian. So, I also installed the matching kernel 
image.

install the headers:

# apt-get install kernel-headers-2.6.8-2-386

and the kernel image that matches with the headers:

#apt-get install kernel-image-2.6.8-2-386

when it asks you "do you want to stop now?--->  SAY "N" and continue.

NOTE: As I do not use any boot loader for my experimental debian setup 
(I boot
if from my other Debian machine) , I can not confirm it, but the new
kernel-image install should modify your grub setting to point to the new
kernel version. If it is not the case, modify /boot/grub/menu.1st to 
point to the new kernel image and initrd image version.
(I would like that someone could verify this)

Now reboot to use the new kernel:

# reboot

When booted, verify that the command:

$ uname -a

gives the 2.6.8-2 version.

Now it is time to install ALSA stuff:

#apt-get install alsa-utils alsa-oss

Note that alsa-utils will install alsa-base as a dependency. Alsa-base 
will prevent from loading the OSS and ALSA drivers at the same
time. (debian uses the "hotplug" and "discover" to do it at boot time).
When installing alsa-base it modifies the "discover" behaviour to
exclude the OSS sound drivers. /etc/discover.d/)

Reboot again just to see everything works.


(This could be really not needed, but it is better to do it to check 
that OSS drivers are unloaded. In my case, before installing ALSA, there 
were OSS and ALSA drivers for my sound card loaded at the same time.

# reboot

Configure the sound card with the "alsaconf" utility. It is very
intuitive to choose your sound card. It will detect it automagically.:

# alsaconf

We are ready to compile svgalib:

Go to the directory in with you have downloaded the sources.


# tar xfvz svgalib-1.9.20
# cd svgalib-1.9.20
# make install
# make demoprogs
# cd demos
# depmod -a

load the svgalib_helper module manually:

# modprobe svgalib_helper

run the test program to see if svgalib works:

# ./vgatest

if it does not work, you should edit /etc/vga/libvga.config file to match
your hardware, but It should do it automatically.


lets test your mouse setup:

#./mousetest

and move your mouse and click  the buttons to see if it works
If it does not work, you have to edit the config file 
/etc/vga/libvga.config and choose your mouse type and mouse device. In 
my case, I commented "mouse Microsoft" and  uncommented "mouse PS2". I 
also changed "/dev/ttyS0" for "/dev/psaux" to point my right mouse PS2 
device.

Now it is ttime to compile Linrad:
Go to your home directory:

$ cd

uncompress the source:

# tar xfvj lir01-33.tbz
# cd linrad-01.33
# ./configure
# make

Note that svgalib_helper module was loaded before.
if not, you can use

#modprobe svgalib_helper

to load it

Run linrad

# ./linrad

and follow Leif directions.

#rmmod svgalib_helper

will unload that module from memory.

You can write a simple bash script and locate it on your linrad 
directory. Call it for example, "runlinrad" and "chmod 755 runlinrad" to 
make it executable.

************************
#!/bin/bash
# script to load module, run linrad, and unload module.
modprobe svgalib_helper
./linrad
rmmod svgalib_helper
************************

So you only need to invoque that script to run Linrad:

./runlinrad

That is all.

Please send me any comments, corrections or suggestions. I will also 
appreciate that you correct my english ;-)

Leif, if possible, I would like to see this guide published somewhere in 
your web page to help Debian hams to setup Linrad.

Thank you very much.

73, Ramiro. EA1ABZ.







#############################################################
This message is sent to you because you are subscribed to
  the mailing list <linrad@antennspecialisten.se>.
To unsubscribe, E-mail to: <linrad-off@antennspecialisten.se>
To switch to the DIGEST mode, E-mail to <linrad-digest@antennspecialisten.se>
To switch to the INDEX mode, E-mail to <linrad-index@antennspecialisten.se>
Send administrative queries to  <linrad-request@antennspecialisten.se>
ennspecialisten.se>
To switch to the DIGEST mode, E-mail to <linrad-digest@antennspecialisten.se>
To switch to the INDEX mode, E-mail to <linrad-index@antennspecialisten.se>
Send administrative queries to  <linrad-request@antennspecialisten.se>
-yµ (you must have root 
>>> privileges do to this !)
>>> Check that you have a symbolic link called build in the
>>> /lib/modules/2.6.x-y-zzz directory.
>>> Ok, now we go back to leif's installation procedure :
>>> cd /usr/src                     ( go to /usr/src )
>>> mkdir svgalib                   ( create a svgalib directory)
>>> cd svgalib                      ( go to that directory)
>>> tar -xvzf /home/<your_user_name>/svgalib-1.9.19.tar.gz
>>> cd svgalib-1.9.19               (this may take a while !)
>>> You have installed svgalib! If your system is new,you need to install
>>> nasm with :
>>> apt-get install nasm
>>> now, we can install linrad itself :
>>> cd /home                        (goto your home directory)
>>> tar -xvjf <your_user_name>/lir01-33.tbz
>>>                                 ( this creates a linrad-01.33 folder )
>>> cd linrad-01.33                 ( go to that directory )
>>> ./configure                     (check dependencies and build 
>>> makefile) make                            ( compile linrad )
>>> make svgalib            ( install svgalib_helper at boot and /dev/svga )
>>> cd /etc/vga
>>> vi libvga.config                ( edit libvga config file )
>>> edit the line beginning  by mouse to select the mouse type, most of us
>>> need : mouse PS2
>>> add a line containing
>>> mdev /dev/input/mice
>>> :wq                             ( save modification and exit editor )
>>> Now is a good time to reboot your system (this will load svgalib_helper)
>>> open a terminal with root privileges :
>>> cd /home/linrad-01.33           ( go to linrad's directory )
>>> ./vgatest                       ( test svgalib config )
>>> ./linrad                        ( enjoy linrad )
>>>
> 
> 
> 



#############################################################
This message is sent to you because you are subscribed to
  the mailing list <linrad@antennspecialisten.se>.
To unsubscribe, E-mail to: <linrad-off@antennspecialisten.se>
To switch to the DIGEST mode, E-mail to <linrad-digest@antennspecialisten.se>
To switch to the INDEX mode, E-mail to <linrad-index@antennspecialisten.se>
Send administrative queries to  <linrad-request@antennspecialisten.se>
@antennspecialisten.se>
To switch to the INDEX mode, E-mail to <linrad-index@antennspecialisten.se>
Send administrative queries to  <linrad-request@antennspecialisten.se>
to woÑ«
> > 
> > Thanks and 73,
> > 
> > Roger
> > W3SZ
> > 
> > 
> 
> sin�Îor linrad usage, you should
>>really sweep a sine generator from zero to beyond the Nyquist
>>frequency of a given converter to determine its aliasing behaviour.
>>
>>Of course, none of this matters if your receiver's (analog) RF/IF/AF
>>filters are steeper and/or narrower than your ADC's anti-aliasing
>>filter...
>>
>>By the way, I am thinking about doing a backend for a linrad/SDR-1000
>>like receiver with A/D converters integrated in the final stage
>>(behind the I/Q demodulator). Not only does this allow to put the ADC
>>in the mast (running S/PDIF-like signals into the shack over Cat5 or
>>fiber), but it also allows hard synchronisation between the sample
>>clock and other receiver clocks, reducing spurs and drift.
>>
>>Regards,
>>
>>JDB.
>>
>>[1] Y<L×@L×@ 96kHz (-48...+48kHz complex bandwidth) from a
>>stereo-sampled I/Q signal on a 96kHz soundcard, but only if you're
>>either willing to accept aliasing noise at the band edges, or if you
>>can build a dual tracking anti-aliasing filter sharper than the sound
>>chip's digital filter (think > 250dB/octave for a good converter).
>>
>>[2] And even 'sampling rate' is a misnomer with modern audio ADCs,
>>seeing that they all use some form of sigma-delta conversion, which
>>(very simply said) is an oversampling lower-order ADC (someta¦
>>1-bit, sometimes multibit) inside a feedback loop, combined with a
>>digital filter/decimator to produce the output samples.
>>--
>>LART. 250 MIPS under one Watt¹¥ee hardware design files.
>>http://www.lart.tudelft.nl/
>>
>>
>>    q¥>
>
i¥ 
>ples.
>>--
>>LART. 250 MIPS under one Watt. Free hardware design files.
>>http://www.lart.tudelft.nl/
>>
>>
>>    
>>
>
>
>
>  
>LiÑÇ  
>> really
>> and [2] I didn's spend enough time on it [only wasted an evening], what  
>> it
>> shows to me is h d"y updatedb, to
> make lookups speedy.
> 
> If you remove the slocate package, you lose the ability to find files in
> a fast way, and have to use the slower find command.
> 
> You could also remove the /etc/cron.daily/slocate.cron, or move it out
> of that directory, say to /root/bin/ and then manually run slocate.cron
> whn pe¸" by the mean of the 'Mozilla Web
> Browser' (see Application - Internet)
> 
> You should download the following files to your persona ff# by he f# by the mean of the 'Mozilla Web
> Browser' (see Application - Internet)
> 
> You should download the following files to your personal folder
> (/home/<your_user_name>) :
> - lir01-33.tbz (linrad itself)
> - svgalib-1.9.19.tar.gz (sri , I haven't tried 1.9.20 yet !)
> 
> (there is no need to download 'nasm' as we can to this with an 'apt-
> get')
> 
> Installing components :
> 
> First, we need to install svgalib but it won't compile unless we install
> a kernel-header package. The command 'apt-cache search kernel-headers'
> will give you all the available packages.If you do not know which one
> should be used do this :
> 
> Switch to the text console #1 (type Ctrl - ALT - F1)
> You should see a prompt asking a login : type root
> Now the password (Type the password of the superuser)
> On the first line, you should see : Linux Debian 2.6.x-y-zzz 
> this is the exact version of your kernel. In my case, I have 2.6.8-2-386
> so in the following, replace the x-y-zzz by the appropriate numbers.
> BTW, you can go back to the graphical mode with Ctrl-Alt-F7
> 
> Intall the kernel-header with the folowing command :
> apt-get install kernel-headers-2.6.x-y-zzz 
> (you must have root privileges do to th¡�)
> 
> Check that you have a symbolic link called build in the
> /lib/modules/2.6.x-y-zzz directory.
> 
> Ok, now we go back to leif's installation procedure :
> cd /usr/src			( go to /usr/src )
> mkdir svgalib			( create a svgalib directory)
> cd svgalib			( go to that directory)
> tar -xvzf /home/<your_user_name>/svgalib-1.9.19.tar.gz
> cd svgalib-1.9.19     		(this may take a while !)
> 
> You have installed svgalib! If your system is new,you need to install
> nasm with :
> apt-get install nasm
> 
> now, we can install linrad itself :
> cd /home			(goto your home directory)
> tar -xvjf <your_user_name>/lir01-33.tbz
> 				( this creates a linrad-01.33 folder )
> cd linrad-01.33 		( go to that directory )
> ./configure			(check dependencies and build makefile) 
> make 				( compile linrad )
> make svgalib		( install svgalib_helper at boot and /dev/svga )
> 
> cd /etc/vga
> vi libvga.config		( edit libvga config file )
> edit the line beginning  by mouse to select the mouse type, most of us
> need : mouse PS2
> add a line containing
> mdev /dev/input/mice
> :wq				( save modification and exit editor )
> 
> Now is a good time to reboot your system (this will load svgalib_helper)
> 
> open a terminal with root privileges :
> cd /home/linrad-01.33		( go to linrad's directory )
> ./vgatest			( test svgalib config )
> ./linrad 			( enjoy linrad )
>  


#############################################################
This message is sent to you because you are subscribed to
  the mailing list <linrad@antennspecialisten.se>.
To unsubscribe, E-mail to: <linrad-off@antennspecialisten.se>
To switch to the DIGEST mode, E-mail to <linrad-digest@antennspecialisten.se>
To switch to the INDEX mode, E-mail to <linrad-index@antennspecialisten.se>
Send administrative queries to  <linrad-request@antennspecialisten.se>
itch to the INDEX mode, E-mail to <linrad-index@antennspecialisten.se>
Send administrative queries to  <linrad-request@antennspecialisten.se>
ons duñÛ the last couple of years.
>>
>>Yesterday I installed Debian-base with the rc3-installer through
>>the network, and it found the PCI-HomePNA-card automatically. The
>>(later) downloaded svgalib-bin package was referred to as 1.4.3-21
>>
>>Next I will expand functionality by trying a linrad 01.33 install.
>>
>>Last week I saw that there was a new svgalib 1.9.20 available.
>>
>>So far I have seen posts only referring to 1.9.19 and earlier.
>>I have had my biggest battles with the 1.9.17 - 1.9.19 helper
>>modules, and indeed I have never succeeded under SuSE/Knoppix.
>>If I remember correctly Gentoo had a distro-matched 1.9.17-r2
>>svgalib package and it worked right away in Gentoo 2004.x
>>
>>This is probably my first posting on the 'Linrad' list, but uÐ*, that a Linux
> system does not need a reboot like the Win-systems. 

No, I think that a reboot is not need. You can always load that module 
by hand with the modprobe command.

But maybe there has
> been a change in this too, or I have never understood the details. This
> proves that reading instructions is very important! In summary: I learnt
> a lot of new things and I arrived at the same result as before, for the
> time being. My impression is that soon there is enough routine to set up
> a 'Linrad' system from state zero ("empty hardware") to full operation
> (one way or the other) in less than 100 minutes. Maybe we should make
> this a small "contest" to create more attention/interest for 'Linrad'.

Good idea.

> 
> 
> Wishing you all a relaxed but productive weekend!  73, "Zaba"  OH1ZAA/2
> 

Well, I have just install Debian in a spare partition last night, so 
today, If I have free time I will try to install last Linrad and last 
svgalib to see.

Just a tip for your X install ( I do not know if knoppix uses the Xfree 
or the Xorg Window system, but it will be helpfull anyway, there should 
not be too much differences). Run knoppix on it. Copy the XF86Config-4 
file to your Debian box. It should work.

Any way, tell me the errors you are having. You also can watch the X log 
errors in /var/log/XFree86.0.log. Look for the "EE" errors, it will tell 
you the reason of the failure.

73, Ramiro.


> 
> At 15:04 15.4.2005 +0200, EA1ABZ wrote:
> 
>> Patrick wrote:
>>
>>> Hello Ramiro and All,
>>> Here is how I install linrad on Sarge.
>>> First I used this install CD :
>>> http://cdimage.debian.org/pub/cdimage-testing/sarge_d-i/i386/rc3/sarge-
>>> i386-netinst.iso
>>
>>
>>
>> Oh yes!, this is my prefered method (100MB), as all base system is 
>> included on the CD and you do not need to download anything to get a 
>> console system running. The business card is even smaller (30 MB), but 
>> you need to download more. The mini.iso is even smaller (8MB) and more 
>> to download.
>>
>>
>> Congratulations for the install report. It will be very useful for the 
>> Debian newbies.
>>
>>
>> Thank you very much.
>>
>> 73, Ramiro.
>>
>> PS: I have just downloaded the rc-3 installer (100MB) and tonight I 
>> will install it to test in another partition.
>>
>>>
>>> The netinst CD-Rom is much quicker than the mini CD . BE AWARE that
>>> these single CD-Rom install tools download most of the packages via FTP
>>> so if you do not have 1Mb/s transfer rate, this may be very sloooow.
>>> When using the netinst CD-Rom, the volume control is working right at
>>> the end of the install process (The meSB1bmRl
ciBnY2M6LSkNCg0KVU5JWCBkb2VzIG5vdCBkaXN0aW5ndWlzaCBiaW5hcnkgZnJvbSB0ZXh0IGZp
bGVzLCB3aGljaCBpcyB3aHkgdGhlICJ0IiBvciAiYiIgaXMgaWdub3JlZC4gSSBqdXN0IA0KbG9v
a2VkIGF0IHRoZSBtYW4gcGFnZSBvbiBmb3BlbiBhbmQgaXQgc2F5cyB0aGUgImIiIGlzIHN0cmlj
dGx5IGZvciBjb21wYXRhYmlsaXR5IHdpdGggQU5TSSBDIGFuZCBoYXMgDQpubyBlZmZlY3Qgb24g
YW55IFBPU0lYIG9wZXJhdGluZyBzeXN0ZW0uIEl0IHN1Z2dlc3RzIGFkZGluZyB0aGUgImIiIGlm
IHlvdSBkbyBJTyBvZiBiaW5hcnkgZmlsZXMgb24gDQpub24tVU5JWCBvcGVyYXRpbmcgc3lzdGVt
cy4gSSdtIG5vdCBzdXJlIGlmIG15IHByb2JsZW1zIHdlcmUgb24gYmluYXJ5IG9yIHRleHQgZmls
ZXMsIGJ1dCBJIGhhdmUgc2VlbiANCnRoZW0uIEJ1dCBBVExDIHdyaXRlcyBiaXRtYXBzLCB3aGlj
aCBhcmUgYmluYXJ5IGZpbGVzLCBzbyBwZXJoYXBzIHRoYXQgaXMgd2hhdCBjYXVzZXMgdGhlIHBy
b2JsZW0uDQoNCj4+Pj4yKSBJZiBpdCBjb21waWxlcyBvbiBXaW5kb3plIGFuZCB5b3VyIGZhdm9y
aXRlIExpbnV4IChSZWRoYXQgb3IgDQo+Pj4+d2hhdGV2ZXIpIGRvbid0IGFzc3VtZSBpdCB3aWxs
IGNvbXBpbGUgDQo+Pj4+b24gYWxsIExpbnV4L1VOSVggc3lzdGVtcy4NCj4+Pg0KPj4+T0suIEFj
dHVhbGx5IGl0IGNvbXBpbGVzIHVuZGVyIExpbnV4IG9ubHkuIA0KPj4NCj4+SSdtIGNvbmZ1c2Vk
LiBZb3UgaGF2ZSBXaW5kb3dzIGJpbmFyaWVzLCBidXQgaXQgb25seSBjb21waWxlcyB1bmRlciBM
aW51eC4NCj4+UGVyaGFwcyB5b3UgdXNlIEN5Z3dpbj8NCj4gDQo+IE5vLCBJIGhhdmUgb25lIGNv
bXB1dGVyIHdpdGggRGViaWFuIExpbnV4LiBPbiB0aGlzIG1hY2hpbmUgSSBoYXZlDQo+IHN2Z2Fs
aWIsIG5hc20gYW5kIG1pbmd3MzIuIEp1c3QgYnkgdHlwaW5nIG1ha2UgImxpbnJhZC5leGUiIHRo
aXMNCj4gY29tcHV0ZXIgcHJvZHVjZXMgbGlucmFkLmV4ZS4NCg0KT0suIEkndmUgbm90IHVzZWQg
dGhhdC4NCg0KPj5Eb2VzIHRoYXQgbWVhbiBvbmx5IFJlZGhhdD8NCj4gDQo+IE9vb2ggTm8hISBJ
dCBtZWFucyBldmVyeSAocmVhc29uYWJsZSkgTGludXggZGlzdHJpYnV0aW9uIHRoYXQgaXMNCj4g
bm90IG11Y2ggb2xkZXIgdGhhbiBSZWRIYXQgNi4xLiANCg0KT0suIEkgaGF2ZSBzZWVuIGEgY29t
bWVudCBmcm9tIHNvbWVvbmUgdGhhdCB0aGV5IGFyZSBoYXBweSBpZiB0aGVpciBjb2RlIGNvbXBp
bGVzIG9uIFJlZGhhdCBhbmQgZG8gbm90IA0Kd29ycnkgYWJvdXQgYW55dGhpbmcgZWxzZS4gVGhh
dCBzZWVtcyBhIGJpdCBtdWNoIHRvIG1lIGlmIHlvdSBhcmUgZ29pbmcgdG8gZGlzdHJpYnV0ZSB0
aGUgY29kZSBhcyANCm9wZW4tc291cmNlLg0KDQo+IEkgb2NjYXNpb25hbGx5IHZlcmlmeSB0aGF0
IHRoZSBjb2RlDQo+IHN0aWxsIHJ1bnMgb24gYW4gb2xkIFBlbnRpdW0gY29tcHV0ZXIgd2l0aCB2
ZXJ5IGxpdHRsZSBtZW1vcnkgb24gd2hpY2gNCj4gaXQgaXMgbm90IHNvIGVhc3kgdG8gaW5zdGFs
bCBhIG1vZGVybiBMaW51eCBkaXN0cmlidXRpb24uDQoNClRoYXQgaXMgc2Vuc2libGUuIEkgd3Jv
dGUgYSBzY3JpcHQgZm9yIGRvaW5nIHRoaXMgaW4gYXRsYy4gVGhlIHNjcmlwdCBsb2dzIGludG8g
YQ0KcmVtb3RlIGhvc3QgYnkgcGFzc3dvcmRsZXNzIChwdWJsaWMta2V5L3ByaXZhdGUta2V5KSBz
c2gsIHJ1bnMgdGhlIGNvbmZpZ3VyZSBzY3JpcHQsIGJ1aWxkcyB0aGUgDQpzb2Z0d2FyZSwgcnVu
cyB0aGUgc2VsZiB0ZXN0cyBhbmQgc2VuZHMgYmFjayB0aGUgcmVzdWx0cyAocGFzc2VzIGFuZCBm
YWlsdXJlcykuIEkgYXNzdW1lIHRoYXQgaXMgbm90IA0KdG9vIGVhc3kgdG8gZG8gd2l0aCBMaW5y
YWQsIGFzIHlvdSBuZWVkIHRvIGJlIGF0IHRoZSBtYWNoaW5lIHRvIHRlc3QgaXQuDQoNCj4+QnV0
IG5ldyBhbGdvcml0aG1zIGFyZSBtb3JlIGxpa2VseSB0byBhcHBlYXIgaWYgbW9yZSBwZW9wbGUg
Y2FuIA0KPj5jb21waWxlIGl0LCB3aGljaCBtZWFucyBtYWtpbmcgaXQgbW9yZSANCj4+cG9ydGFi
bGUuIEkgdHJpZWQgY29tcGlsaW5nIGl0IHVuZGVyIFNvbGFyaXMgb24gU1BBUkMgYW5kIHNvb24g
DQo+PnJlYWxpc2VkIGl0IHdhcyB2ZXJ5IExpbnV4IGRlcGVuZGFudC4gSSANCj4+Z2F2ZSB1cCBh
dCB0aGF0IHBvaW50LiBJIGFwcHJlY2FpdGUgdGhlIG51bWJlciBvZiBTUEFSQyB1c2VycyBmb3Ig
DQo+PmhhbSBzb2Z0d2FyZSBtdXN0IGJlIHF1aXRlIGxvdywgYnV0IA0KPj5pZiB0aGUgY29kZSBv
bmx5IGNvbXBpbGVzIG9uIFJlZGhhdCwgeW91IGFyZSBzZXJpb3VzbHkgDQo+PnJlc3RyaWN0aW5n
IHRoZSB1c2VyIGJhc2UuDQo+IA0KPiBTdXJlbHkgdHJ1ZSwgYnV0IHRoYXQgaXMgbm90IHRoZSBj
YXNlLiBJIGhhdmUgdGVzdGVkIHNldmVyYWwgb2YgZWFjaCBvZg0KPiBSZWRIYXQsIE1hbmRyYWtl
LCBTdXNlLCBGZWRvcmEsIERlYmlhbiBhbmQgU2xhY2t3YXJlLiBUaGVyZSBoYXZlIGJlZW4NCj4g
c2V2ZXJhbCBidWdzIGluIHZhcmlvdXMgZGlzdHJpYnV0aW9ucyBhbmQgSSBoYXZlIG1hZGUgdGhl
IGNoYW5nZXMNCj4gcmVxdWlyZWQgdG8gbWFrZSBMaW5yYWQgY29tcGlsZSB1bmRlciBhbGwgb2Yg
dGhlbS4gVGhlcmUgaGF2ZSBhbHNvIGJlZW4NCj4gcXVpdGUgYSBsb3Qgb2YgZXJyb3JzIGluIHRo
ZSBzb3VuZCBzeXN0ZW1zIG92ZXIgdGhlIHllYXJzIGFuZCB0aGVyZWZvcmUNCj4gdGhlIHNvdW5k
Y2FyZCBpbml0IHJvdXRpbmUgaXMgcXVpdGUgYSBiaXQgbW9yZSBjb21wbGljYXRlZCB0aGFuIHdv
dWxkIGJlDQo+IG5lZWRlZCBvbiBhIG1vZGVybiBkaXN0cmlidXRpb24uDQoNCk9LLCB0aGluZ3Mg
YXJlIGNsZWFyIG5vdy4NCg0KPiBUaGUgbWVzc2FnZSBJIHRyaWVkIHRvIGNvbnZleSBpcyB0aGF0
IGl0IGlzIGV4dHJlbWVseSBlYXN5IGZvciBhIG5ld2NvbWVyDQo+IHdpdGggcHJhY3RpY2FsbHkg
bm8gcHJvZ3JhbW1pbmcgZXhwZXJpZW5jZXMgdG8gY2hhbmdlIHRoZSBMaW5yYWQgY29kZS4NCj4g
Q2VydGFpbmx5IGl0IGlzIG5vdCBlYXN5IHRvIGNoYW5nZSB0aGUgYWN0dWFsIHByb2Nlc3Npbmcg
aW4gYSBtZWFuaW5nZnVsDQo+IHdheSwgYnV0IHNlbmRpbmcgY29tbWFuZHMgdG8gYSB0cmFubWl0
dGVyIG92ZXIgdGhlIHNlcmlhbCBwb3J0IG9yIHNob3dpbmcNCj4gc29tZSBtb3JlIGluZm9ybWF0
aW9uIG9uIHRoZSBzY3JlZW4gaXMgdmVyeSBlYXN5LiBFYXNpZXN0LCB3cml0ZSBhIGxpbmUNCj4g
YXQgdGhlIHRvcCBvZiB0aGUgc2NyZWVuICJUSElTIENPUFkgT0YgTElOUkFEIEhBUyBCRUVOIEhB
Q0tFRCBCWSBYWFhYWCIuDQo+IElmIEkgd2VyZSBhIDE0IHllYXJzIG9sZCBuZXdjb21lciBJIG1p
Z2h0IGhhdmUgc3RhcnRlZCBhdCBzb21ldGhpbmcgDQo+IGxpa2UgdGhhdCB0byBnaXZlIHRvIG15
IGZyaWVuZHM7LSkgU2hvd2luZyB0aW1lLCBkYXRlLCBwYXJhbWV0ZXIgdmFsdWVzDQo+IG9yIGFu
eSBvdGhlciBnbG9iYWwgZGF0YSBpcyBhbHNvIHZlcnkgZWFzeS4uLi4NCg0KSSdkIG1pcy1pbnRl
cnByZXRlZCB3aGF0IHlvdSB3ZXJlIHNheWluZy4gU29ycnkgYWJvdXQgdGhhdC4gSXQncyBwcm9i
YWJseSBub3QgaGVscGVkIGJ5IHRoZSBmYWN0IEkgDQpkb24ndCBhY3R1YWxseSBydW4gdGhlIGNv
ZGUuIEkgbG9va2VkIGF0IHVzaW5nIHNvbWUgb2YgaXQgZm9yIGEgcHJvZmVzc2lvbmFsIGFwcGxp
Y2F0aW9uLCBidXQgbmV2ZXIgZGlkLg0KDQotLSANCkRyLiBEYXZpZCBLaXJrYnkgUGhEIENFbmcg
TUlFRSwNClNlbmlvciBSZXNlYXJjaCBGZWxsb3csDQpEZXBhcnRtZW50IG9mIE1lZGljYWwgUGh5
c2ljcywNCk1hbGxldCBQbGFjZSBFbmdpbmVlcmluZyBCdWlsZGluZywNCkdvd2VyIFN0LA0KVW5p
dmVyc2l0eSBDb2xsZWdlIExvbmRvbiwNCkxvbmRvbiBXQzFFIDZCVC4NCg0KDQojIyMjIyMjIyMj
IyMjIyMjIyMjIyMjIyMjIyMjIyMjIyMjIyMjIyMjIyMjIyMjIyMjIyMjIyMjIyMjIyMjDQpUaGlz
IG1lc3NhZ2UgaXMgc2VudCB0byB5b3UgYmVjYXVzZSB5b3UgYXJlIHN1YnNjcmliZWQgdG8NCiAg
dGhlIG1haWxpbmcgbGlzdCA8bGlucmFkQGFudGVubnNwZWNpYWxpc3Rlbi5zZT4uDQpUbyB1bnN1
YnNjcmliZSwgRS1tYWlsIHRvOiA8bGlucmFkLW9mZkBhbnRlbm5zcGVjaWFsaXN0ZW4uc2U+DQpU
byBzd2l0Y2ggdG8gdGhlIERJR0VTVCBtb2RlLCBFLW1haWwgdG8gPGxpbnJhZC1kaWdlc3RAYW50
ZW5uc3BlY2lhbGlzdGVuLnNlPg0KVG8gc3dpdGNoIHRvIHRoZSBJTkRFWCBtb2RlLCBFLW1haWwg
dG8gPGxpbnJhZC1pbmRleEBhbnRlbm5zcGVjaWFsaXN0ZW4uc2U+DQpTZW5kIGFkbWluaXN0cmF0
aXZlIHF1ZXJpZXMgdG8gIDxsaW5yYWQtcmVxdWVzdEBhbnRlbm5zcGVjaWFsaXN0ZW4uc2U+DQoA
ZSAoGwAAKBsAAGxlaWZAc201YnN6LmNvbSB3cm90ZToKPiBIaSBEYXZpZCwKCkggTGVpZiwKCj4+
V2h5IGlzIGl0IHBvc3NpYmxlIHVuZGVyIExpbnV4IG9ubHkgPwo+IAo+IEhtbW0sIHdoYXQgSSBt
ZW50IGlzIHRoYXQgYW4gYXZlcmFnZWx5IHNraWxsZWQgcmFkaW8gYW1hdGV1ciBjYW4KPiBtYWtl
IGNoYW5nZXMgdG8gdGhlIExpbnJhZCBzb3VyY2UgY29kZSwgdHltZSAibWFrZSBsaW5yYWQuZXhl
IiAKPiBhbmQgZ2V0IHNvbWV0aGluZyB0aGF0IHdpbGwgd29yayBvbiB0aGUgV2luZG93cyBtYWNo
aW5lLgoKCk9LLCBJIGdldCB5b3UuIEkgd291bGQgYWdyZWUgYnVpbGRpbmcgY29kZSBvbiBVTklY
IGlzIHZlcnkgZWFzeSAtIGZhciBsZXNzIGhhc3NsZSB0aGFuIG9uIFdpbmRvemUuIFRoZSAKJ2Nv
bmZpZ3VyZScgc2NyaXB0cyB3b3JrIHByZXR0eSB3ZWxsLiBUaGV5IGFyZSBtdWNoIGVhc2llciB0
aGFuIGhhY2tpbmcgTWFrZWZpbGVzLgoKPiBPZiBjb3VyZXMgYW55b25lIHdpdGggYWRlcXVhdGUg
Y29tcHV0aW5nIHNraWxzIGNhbiBkbyB3aGF0ZXZlciAKPiBpdCB0YWtlcyB0byBpbnN0YWxsIHRo
ZSBzb3VyY2UgZmlsZXMsIGEgc3VpdGFibGUgQyBjb21waWxlcgo+IGFuZCBuYXNtIGZvciBNUyBX
aW5kb3dzIGFuZCB0aGVuIHNldCB1cCBhIG1ha2VmaWxlLiAKClN1cmUuCgo+IE9mIGNvdXJzZSBJ
IG11c3QgYWdyZWUgdGhhdCAicG9zc2libGUgdW5kZXIgTGludXgiIG1pZ2h0IGJlCj4gYSBzZXJp
b3VzIG92ZXJzdGF0ZW1lbnQgYnV0IEkgdGhpbmsgeW91IHdpbGwgZmluZCB0aGF0IHRoaXMKPiB3
aWxsIGJlIHNvIGZyb20gYSBwcmFjdGljYWwgcG9pbnQgb2Ygdmlldy4gCgpJIGFtIGdsYWQgdG8g
aGVhciB0aGF0LiBJIGhhdmUgaGVyZCBpcyBzYWlkIHNvbWUgaGF2ZSBpbnN0YWxsZWQgTGludXgg
Zm9yIExpbnJhZCwgd2hpY2ggY2FuIG9ubHkgYmUgYSAKZ29vZCB0aGluZy4gSSBzaG91bGQgYWRk
IEkgZG8gbm90IHJ1biBMaW51eCBtdWNoLiBJIHVzZSBpdCBhdCB3b3JrIG9uIG15IFBDLCBidXQg
YXQgaG9tZSBJIHVzZSAKU29sYXJpcy4gKE1vc3QgcGVvcGxlIHdvdWxkIG5vIGRvdWJ0IGRvIGl0
IHRoZSBvdGhlciB3YXkgYXJvdW5kIC0gU29sYXJpcyBhdCB3b3JrLCBMaW51eCBhdCBob21lISkK
Cj4+RnJvbSBteSBleHBlcmllbmNlIHdpdGggYXRsYywgdGhlcmUgYXJlIHBlcmhhcHMgMTAwIHVz
ZXJzLCBidXQgSSAKPj5zdXNwZWN0IG9ubHkgYSBmZXcgcGVyY2VudCBvZiB0aGVtINmlAQBmeSB0
aGUgY29kZS4KPiAKPiBBIGNvbnNpZGVyIGEgZmV3IHBlcmNlbnQgcXVpdGUgc3VjZXNzZnVsLiAK
Cj4gUHJlc3VtYWJseSB0aGUgcmVhc29ucwo+IGZvciBwZXJzb25hbGl6aW5nIGF0bGMgYXJlIHJh
dGhlciBzbWFsbCBhcyBjb21wYXJlZCB0byBMaW5yYWQuCgpZZXMsIEkgdGhpbmsgdGhhdCBpcyB0
cnVlLgoKPj4+PjEpIElmIHlvdSB3cml0ZSB0ZXh0IGZpbGVzLCB1c2UgZnA9Zm9wZW4oImZvbyIs
InJ0Iikgb3IgCj4+Pgo+PmZvcGVuKCJmb28iLCJ3dCIpLgo+Pgo+Pj4+VU5JWCBzaWxlbnRseSBp
Z25vcmVzIHRoZSAidCIgZm9yIHRleHQgb3IgImIiIGZvciBiaW5hcnksIGJ1dCBmb3IgCj4+Pj5X
aW5kb3dzIGl0IGlzIGltcG9ydGFudC4KPj4+Cj4+PkhtbW0sIEkgYW0gb3BlbmluZyB0aGUgdGV4
dCBma‰pyBsaWtlIHRoaXM6IGZvcGVuKCJmb28iLCJ3Iikgb3IKPj4+Zm9wZW4oImZvbyIsInIi
KS4gSSBoYXZlIG5vdCBub3RpY2VkIGFueSBwcm9ibGVtcyBvdGhlciB0aGFuCj4+PnRoZSB1c3Vh
bCBvbmUgdGhhdCBXaW5kb3dzIHVzZXMgcmV0dXJuIGFuZCBsaW5lLWZlZWQgd2hpbGUgCj4+Pkxp
bnV4IG9ubHkgdXNlcyBvbmUgb2YgdGhlbS4KPj4KPj5JJ3ZlIGNlcnRhaW5seSBzZWVuIHByb2Js
ZW1zLiBJdCBtYXkgaGF2ZSBiZWVuIHdyaXRpbmcgYmluYXJ5IAo+PmZpbGVzLCBJIGNhbid0IHJl
Y2FsbC4gQnV0IEkgdGhpbmsgaXQgaXMgCj4+c2FmZXIgdG8gcHV0IHRoZSAidCIgb3IgImIiLiBU
aGUgc29mdHdhcmUgSSB3cm90ZSBmb3IgCj4+dHJhbnNtaXNzaW9uIGxpbmVzIHdhcyBub3Qgd29y
a2luZyBwcm9wZXJseSBvbiAKPj5ET1MgYW5kIHdhcyBmb3VuZCB0byBiZSB0aGUgbGFjayBvZiB0
aGUgInQiIChvciB3YXMgaXQgImIiID8/KSAKPj5vcHRpb24uIEFkZGluZyBpdCBnb3QgaXQgd29y
a2luZyAKPj5wcm9wZXJseSBvbiBib3RoIHBsYXRmb3Jtcy4KPiAKPiBNYXliZSBpdCBpcyBiZWNh
dXNlIEkgdXNlIHNvbWUgdmVyc2lvbiBvZiBnY2MgdW5kZXIgbWluZ3czMi4KPiBJIGtub3cgdGhh
dCB1bmRlciBET1MgYSBzaW5nbGUgb2NjdXJhbmNlIG9mIGN0bCBaIGlzIGludGVycHJldGVkIAo+
IGFzIGVuZCBvZiBmaWxlIHNvIGEgYmluYXJ5IGZpbGUgaXMgbmV2ZXIgcmVhZCBmdXJ0aGVyIHRo
YW4gdG8KPiB0aGUgZmlyc3Qgb2NjdXJhbmNlIG9mIDI2IGlmIGl0IGlzIG9wZW5lZCBhcyBh